## Slide 1: Design Point Cycle Model
TEAM 1: NIGHT RAVENS
LAUREN MARTINS & JOHN CLARDY

## Slide 2: Final Selected Parameters
Design Point:
  Cruise: 38,000 ft
  Mach: 0.65
  Standard Temperature
Parameters | Values
OPR | 17.15
TET [K] | 1700
FPR | 2.5
BPR | 1.2

## Slide 3: Performance metrics
Parameters | Excel Values | Gas Turb Values
Thrust [kN] | 7.596 | 7.34
Specific Thrust [N*s/kg] | 528.41 | N/A
TSFC [g/(kN*s)] | 25.57 | 26.1564

## Slide 4: H-S (mollier) diagram
tbd
tbd

## Slide 5: Efficiency assumptions
Parameters | Values
Fan/LPC Polytropic Efficiency | 0.92
IPC Polytropic Efficiency | 0.9
Combustion Efficiency | 0.99
HPT Polytropic Efficiency | 0.9
HPC Polytropic Efficiency | 0.88

## Slide 6: Bleed flow assumptions
Gas Turb Cooling Presets
Parameters | Values [% core flow]
LPT Cooling | 3
NGV Cooling | 5
HPT Cooling | 5

## Slide 7: Additional loss assumptions
Parameters | Values [% core flow]
(Swan neck loss coefficient) | 2
(Combustor total pressure loss) | 2
Parameters | Values [% core flow]
 | 2
 | 2

## Slide 8: Thermodynamic properties

## Slide 9: Total pressure
Chart: Total Pressure Comparision
Excel | 20.6458 | 27.4314 | 26.8827 | 67.2068 | 67.2068 | 65.8627 | 461.0388 | 451.818 | 451.818 | 299.9424 | 269.9481 | 269.9481 | 65.8627 | 64.5454 | 64.5454
GasTurb | 20.646 | 27.43 | 26.882 | 67.205 | 67.205 | 66.533 | 465.728 | 451.756 | 451.756 | 213.294 | 209.028 | 126.032 | 65.188 | 75.339 | 75.339

## Slide 10: Total temperature
Chart: Total Temprature Comparison
Excel | 216.65 | 235.0243 | 235.0243 | 312.6231 | 312.6231 | 312.6231 | 573.9512 | 1700 | 1645.0061 | 1402.0087 | 1402.0087 | 1372.4912 | 312.6231 | 798.3084 | 798.3084
GasTurb | 216.65 | 235 | 235 | 312.42 | 312.42 | 312.42 | 581.99 | 1700 | 1647.37 | 1378.88 | 1378.88 | 1221.25 | 312.42 | 760.92 | 760.92

## Slide 11: Inlet Face (1)
Parameters | Excel Values | Gas Turb Values
[K] | 235.02 | 235
[kJ/kg] | 235.24 | N/A
Mass Flow [kg/s] | 14.99 | 14.69
Corrected Mass Flow [kg/s] | 50 | 50
Parameters | Excel Values | Gas Turb Values
 | 235.02 | 235
 | 235.24 | N/A
Mass Flow [kg/s] | 14.99 | 14.69
Corrected Mass Flow [kg/s] | 50 | 50

## Slide 12: HPC Inlet (2.6)
Parameters | Excel Values | Gas Turb Values
[K] | 312.62 | 312.42
[kJ/kg] | 313.07 | 14.377
Mass Flow [kg/s] | 6.677 | 6.677
Corrected Mass Flow [kg/s] | 10.70 | 10.59
Parameters | Excel Values | Gas Turb Values
 | 312.62 | 312.42
 | 313.07 | 14.377
Mass Flow [kg/s] | 6.677 | 6.677
Corrected Mass Flow [kg/s] | 10.70 | 10.59

## Slide 13: HPC Discharge diffuser (3.1)
Parameters | Excel Values | Gas Turb Values
[K] | 573.95 | 581.99
[kJ/kg] | 579.91 | 290.06
Mass Flow [kg/s] | 5.764 | 6.476
Corrected Mass Flow [kg/s] | 1.788 | 2.002
Parameters | Excel Values | Gas Turb Values
 | 573.95 | 581.99
 | 579.91 | 290.06
Mass Flow [kg/s] | 5.764 | 6.476
Corrected Mass Flow [kg/s] | 1.788 | 2.002

## Slide 14: NGV Cool Pre-Throat (4.05)
Parameters | Excel Values | Gas Turb Values
[K] | 1645.0 | 1647.4
[kJ/kg] | 1884.4 | ~1662.9 (4)
Mass Flow [kg/s] | 6.253 | 6.301
Corrected Mass Flow [kg/s] | 3.351 | 3.379
Parameters | Excel Values | Gas Turb Values
 | 1645.0 | 1647.4
 | 1884.4 | ~1662.9 (4)
Mass Flow [kg/s] | 6.253 | 6.301
Corrected Mass Flow [kg/s] | 3.351 | 3.379

## Slide 15: LPT Inlet (4.8)
Parameters | Excel Values | Gas Turb Values
[K] | 1402.0 | 1378.9
[kJ/kg] | 1573.6 | 1243.1
Mass Flow [kg/s] | 6.577 | 6.635
Corrected Mass Flow [kg/s] | 5.445 | 7.036
Parameters | Excel Values | Gas Turb Values
 | 1402.0 | 1378.9
 | 1573.6 | 1243.1
Mass Flow [kg/s] | 6.577 | 6.635
Corrected Mass Flow [kg/s] | 5.445 | 7.036

## Slide 16: Mixer (6)
Parameters | Excel Values | Gas Turb Values
[K] | 798.31 | 760.92
[kJ/kg] | 873.62 | 488.82
Mass Flow [kg/s] | 14.79 | 14.85
Corrected Mass Flow [kg/s] | 38.64 | N/A
Parameters | Excel Values | Gas Turb Values
 | 798.31 | 760.92
 | 873.62 | 488.82
Mass Flow [kg/s] | 14.79 | 14.85
Corrected Mass Flow [kg/s] | 38.64 | N/A
Gas Turb has no Station 7 data
  Mixer (Station 6) was chosen as stand-in for core nozzle inlet
  Lacked Corrected Mass Flow value

## Slide 17: References
“Aero L-39 Skyfox.” Wikipedia, Wikimedia Foundation, 17 Jan. 2026, en.wikipedia.org/wiki/Aero_L-39_Skyfox.
“AIDC T-5 Brave Eagle.” Wikipedia, Wikimedia Foundation, 26 Jan. 2026, en.wikipedia.org/wiki/AIDC_T-5_Brave_Eagle.
“On-design Cycle Analysis of a Turbofan Engine.” Course notes, Embry-Riddle Aeronautical University, n.d.

## Slide 18: THANK YOU
Are there any questions?