## Slide 1: Final design review
TEAM 1: NIGHT RAVENS
LAUREN MARTINS & JOHN CLARDY

## Slide 2: Requirements specification
Design Point:
  Cruise: 38,000 ft
  Mach: 0.65
  Standard Temperature
Parameters | Values
Maximum Engine Front Face Diameter | 25 in (0.635 m)
Maximum Engine Length | 137.795 in (3.5 m)
Required Installed Thrust @ Cruise | 1326.9 lbf (5902.3 N)
Notes: During presentation, talk about how all of these influenced design decisions

## Slide 3: Constraint analysis
Design Point:
  (57.7, 0.37)
Notes: During presentation, talk about how all of these influenced design decisions

## Slide 4: Methodology

## Slide 5: Methodology
Gas Model:
Pseudo-perfect. Specific heat is treated as a function of T & FAR, but independent from P.
Simplifying Assumptions:
Ideal gas, adiabatic components, polytropic efficiency
Installation Effects:
Add 5% of thrust to get required thrust

## Slide 6: Performance Specifications
Airframe |  |  | 
K1 | K2 | CD0 | CDR
0.18 | 0 | 0.014 | 0
Max Climb Rate:
  23,367 ft/min at M = 0.800, h = 0 ft
Acceleration:
  4.355 m/s² (0.444 g) at M = 0.487, h = 0 ft
Parameters | Values
Thrust | 1371.3 lbf (6.10 kN)
Specific Thrust | 1362.5 ft/s (415.28 m/s)
TSFC | 0.758 (lbm/hr)/lbf (21.46 g/(kN*s))

## Slide 7: Performance Specifications
TOGW: 13585 lb
Chart: Aircraft Weight vs Mission Time
| 0.02 | 0.05 | 0.08 | 0.11 | 0.14000000000000001 | 0.17 | 1.67 | 1.77 | 1.87 | 1.9700000000000002 | 2.14 | 2.89 | 2.99 | 3.0900000000000003 | 3.14 | 3.1550000000000002 | 3.165
 | 13533.1123 | 13450.4198 | 13382.0177 | 13323.4561 | 13273.6539 | 13236.3067 | 11854.7485 | 11810.4757 | 11762.9928 | 11706.66 | 11300.0334 | 10609.2543 | 10530.9417 | 10410.7966 | 10344.7866 | 10327.8397 | 10327.8397
tsfc | 0.64675 | 0.7782 | 0.75747 | 0.77035 | 0.81278 | 0.84028 | 0.75326 | 0.67163 | 0.65534 | 0.66346 | 0.74193 | 0.75326 | 0.68766 | 0.71311 | 0.71311 | 0.66595 | 0.82072

## Slide 8: Performance Specifications

## Slide 9: Engine Sizing

## Slide 10: Space Claim
Parameter | Value | Value
Overall space claim | 30.23 in | 0.768 m
Length | 137.05 in | 3.481 m
Expected Weight | 1914.6 lb | 868.5 kg

## Slide 11: intake
Parameter | Value
A1 Area | 418.5 in2 (0.27 m2)
A2 Area | 573.5 in2 (0.37 m2)
Athroat Area | 263.5 in2 (0.17 m2)
A1 Diameter | 0.5832 m (22.96 in)
A2 Diameter | 0.6881 m (27.09 in)
Athroat | 0.4684 m 18.44 in
Intake Pressure Recovery | 0.9104%

## Slide 12: Combustor
Parameters | Values
Volume | 0.029 m3
Cross-Sectional Area | 0.02171 m2
Length of Combustor | 1.35 m (53.14in)
Estimated Loss | ~5%
Expected Loading @ Design Point | 2.0249
Relight Capability @ Design Point | Yes
NOTE: Based on the preliminary analysis done so far on the combustor, it appears that relight should be possible at any point along the entire mission.
Notes: In research, the loading seems to be really low for the usual jet trainer, and the length of the combustor seems to be particularly large compared to the usual engine. This would be something to work on in future designs to see if the engine can be made smaller

## Slide 13: Thermodynamic cycle
Chosen design point
Engine architecture
2-Spool Mixed Turbofan
Non-Afterburning
Cruise: 38,000 ft
Mach: 0.65
Standard Temperature
Optimize Cruise TSFC

## Slide 14: Parametric studies

## Slide 15: Sensitivity – bleeds
Study | Base | Delta | SFC% | Sp. Thrust%
Rel. Overboard Bleed W_Bld/W25 | 0.01 | 0.01 | 0.53 | -1.79
HPT NGV 1 Cooling Air / W25 | 0.05 | 0.01 | -0.42 | -0.85
HPT Rotor 1 Cooling Air / W25 | 0.05 | 0.01 | -0.27 | -0.99
LPT Rotor 1 Cooling Air / W25 | 0.05 | 0.01 | -0.28 | -0.99
Rel.HP Leakage to LPT exit | 0.05 | 0.01 | -0.16 | -1.11

## Slide 16: Sensitivity – component eff.
Study | Base | Delta | SFC% | SpThrust%
Polytr.Inner LPC Efficiency | 0.92 | -0.01 | 0.06 | -0.28
Polytr.Outer LPC Efficiency | 0.92 | -0.01 | 0.1 | -0.1
Polytr. HPC Efficiency | 0.88 | -0.01 | 0.15 | -0.72
Polytr. HPT Efficiency | 0.9 | -0.01 | 0.26 | -0.25
Polytr. LPT Efficiency | 0.91 | -0.01 | 0.17 | -0.17
Polytr.Inner LPC Efficiency | 0.92 | 0.01 | -0.05 | 0.27
Polytr.Outer LPC Efficiency | 0.92 | 0.01 | -0.1 | 0.1
Polytr. HPC Efficiency | 0.88 | 0.01 | -0.13 | 0.68
Polytr. HPT Efficiency | 0.9 | 0.01 | -0.24 | 0.24
Polytr. LPT Efficiency | 0.91 | 0.01 | -0.16 | 0.16
Burner Design Efficiency | 0.9995 | -0.01 | 0.95 | 0.06

## Slide 17: Sensitivity – Pr
Study | Base | Delta | SFC% | SpThrust%
Inner Fan Pressure Ratio | 2.8 | 0.1 | -0.45 | -0.25
Outer Fan Pressure Ratio | 2.8 | 0.1 | -0.42 | 0.42
Design Bypass Ratio | 1.41961 | 0.2 | -2.67 | -5.1
HP Compressor Pressure Ratio | 10.5138 | 0.1 | -0.12 | -0.08

## Slide 18: Final parameters
Parameters | Values
OPR | 29
TET | 1606 K
FPR | 2.8
BPR | 1.4

## Slide 19: H-s (mollier) diagram

## Slide 20: Component efficiencies
Parameters | Values
Fan/LPC Polytropic Efficiency | 0.92
HPC Polytropic Efficiency | 0.88
Combustion Efficiency | 0.99
HPT Polytropic Efficiency | 0.9
LPT Polytropic Efficiency | 0.91

## Slide 21: Bleed flow assumptions

## Slide 22: Additional losses
Parameters | Values [%]
(Swan neck loss coefficient) | 2
(Combustor total pressure loss) | 2
Parameters | Values [%]
 | 2
 | 2

## Slide 23: Thermodynamic properties

## Slide 24: Mach assumptions
Location | Mach
Fan Inlet | 0.5
Fan Exit | 0.52
HPC Inlet & Exit | 0.55
Burner Exit & HPT Exit | 0.4
LPT Exit | 0.5
Bypass | 0.5

## Slide 25: Pressure & Temperature

## Slide 26: fAN Face (2)
Parameters | Gas Turb Values
[K] | 235
[kJ/kg] | -63357
Mass Flow [kg/s] | 14.69
Corrected Mass Flow [kg/s] | 50
Parameters | Gas Turb Values
 | 235
 | -63357
Mass Flow [kg/s] | 14.69
Corrected Mass Flow [kg/s] | 50

## Slide 27: HPC Inlet (25)
Parameters | Gas Turb Values
[K] | 323.57
[kJ/kg] | 25625
Mass Flow [kg/s] | 6.07
Corrected Mass Flow [kg/s] | 8.75
Parameters | Gas Turb Values
 | 323.57
 | 25625
Mass Flow [kg/s] | 6.07
Corrected Mass Flow [kg/s] | 8.75

## Slide 28: Combustor Inlet(3)
Parameters | Gas Turb Values
[K] | 682.16
[kJ/kg] | 396123
Mass Flow [kg/s] | 5.77
Corrected Mass Flow [kg/s] | 1.15
Parameters | Gas Turb Values
 | 682.16
 | 396123
Mass Flow [kg/s] | 5.77
Corrected Mass Flow [kg/s] | 1.15

## Slide 29: COMBUSTOR exit(4)
Parameters | Gas Turb Values
[K] | 1606.68
[kJ/kg] | 1528220
Mass Flow [kg/s] | 4.93
Corrected Mass Flow [kg/s] | 1.551
Parameters | Gas Turb Values
 | 1606.68
 | 1528220
Mass Flow [kg/s] | 4.93
Corrected Mass Flow [kg/s] | 1.551

## Slide 30: LPT Inlet (45)
Parameters | Gas Turb Values
[K] | 1174.73
[kJ/kg] | 981613
Mass Flow [kg/s] | 5.53
Corrected Mass Flow [kg/s] | 5.36
Parameters | Gas Turb Values
 | 1174.73
 | 981613
Mass Flow [kg/s] | 5.53
Corrected Mass Flow [kg/s] | 5.36

## Slide 31: eXIT (8)
Parameters | Gas Turb Values
[K] | 595.23
[kJ/kg] | 306810
Mass Flow [kg/s] | 14.76
Corrected Mass Flow [kg/s] | 27.601
Parameters | Gas Turb Values
 | 595.23
 | 306810
Mass Flow [kg/s] | 14.76
Corrected Mass Flow [kg/s] | 27.601

## Slide 32: Engine design tables

## Slide 33: Engine cycle performance
Case | Pamb [kPa] | Tamb [K] | M0 | TET [K] | OPR | FPR | BPR | Fnet [kN] | Fnet [lbf] | TSFC [g/kNs] | TSFC [(lbm/hr)/lbf] | FAR
SLS | 101.33 | 288.15 | 0.00 | 1850.00 | 30.22 | 2.84 | 1.35 | 30.95 | 6958.83 | 18.07 | 0.6381 | 0.01127
RTO | 90.81 | 282.25 | 0.20 | 1638.90 | 24.46 | 2.48 | 1.49 | 20.25 | 4551.93 | 18.32 | 0.6468 | 0.00883
TOC | 18.75 | 216.70 | 0.55 | 1850.00 | 38.65 | 3.31 | 1.21 | 7.27 | 1634.71 | 23.62 | 0.8339 | 0.01259
CRZ | 20.65 | 216.70 | 0.65 | 1543.89 | 28.65 | 2.77 | 1.43 | 5.98 | 1345.25 | 21.34 | 0.7533 | 0.00874

## Slide 34: fan
Case | Ptin [kPa] | Ttin [K] | W [kg/s] | Wcorr [kg/s] | PR | Power [kW] | Eff [Poly] | Nmech [%]
SLS | 99.30 | 288.15 | 49.64 | 50.65 | 2.84 | 5612.25 | 0.9044 | 113.48
RTO | 91.51 | 284.47 | 41.99 | 46.19 | 2.48 | 3770.57 | 0.9519 | 99.21
TOC | 22.58 | 229.79 | 13.64 | 54.67 | 3.31 | 1669.45 | 0.8035 | 121.20
CRZ | 26.88 | 235.00 | 14.60 | 49.70 | 2.77 | 1275.13 | 0.9262 | 98.92

## Slide 35: compressor
Case | Ptin [kPa] | Ttin [K] | W [kg/s] | Wcorr [kg/s] | PR | Power [kW] | Eff [Poly] | Nmech [%]
SLS | 278.95 | 400.32 | 21.16 | 9.06 | 10.76 | 9356.23 | 0.8743 | 114.46
RTO | 225.18 | 373.59 | 16.85 | 8.63 | 9.94 | 6516.37 | 0.8872 | 105.91
TOC | 73.80 | 351.50 | 6.16 | 9.34 | 11.82 | 2628.79 | 0.8539 | 111.90
CRZ | 73.82 | 321.94 | 6.00 | 8.70 | 10.43 | 2197.31 | 0.8809 | 99.31

## Slide 36: HPT
Case | Ptin [kPa] | Ttin [K] | W [kg/s] | Wcorr [kg/s] | ER | Power [kW] | Eff [Poly] | Nmech [%]
SLS | 2908.85 | 1850.00 | 18.33 | 1.62 | 3.55 | 9860.29 | 0.9047 | 114.46
RTO | 2167.53 | 1638.90 | 14.53 | 1.62 | 3.56 | 6901.18 | 0.9033 | 105.91
TOC | 847.67 | 1850.00 | 5.35 | 1.62 | 3.51 | 2850.31 | 0.9029 | 111.90
CRZ | 746.97 | 1543.89 | 5.17 | 1.62 | 3.53 | 2286.22 | 0.8996 | 99.31

## Slide 37: LPT
Case | Ptin [kPa] | Ttin [K] | W [kg/s] | Wcorr [kg/s] | ER | Power [kW] | Eff [Poly] | Nmech [%]
SLS | 803.16 | 1405.53 | 19.39 | 5.40 | 2.34 | 5668.93 | 0.9333 | 113.48
RTO | 596.88 | 1237.16 | 15.37 | 5.41 | 2.27 | 3808.65 | 0.9324 | 99.21
TOC | 236.52 | 1407.47 | 5.65 | 5.35 | 2.44 | 1686.30 | 0.9055 | 121.20
CRZ | 207.65 | 1163.60 | 5.46 | 5.36 | 2.34 | 1288.01 | 0.9107 | 98.92

## Slide 38: References
“On-design Cycle Analysis of a Turbofan Engine.” Course notes, Embry-Riddle Aeronautical University, n.d.
“Gas Turb 14 Manual.” Gas Turb, 4 April. 2026, https://www.gasturb.com/Downloads/Manuals/GasTurb14.pdf.
“Gas Turbine Combustors.” Course notes, Embry-Riddle Aeronautical University, n.d.
“AE440_Inlets.” Course notes, Embry-Riddle Aeronautical University, n.d.

## Slide 39: THANK YOU
Are there any questions?